Memory and Resource Efficient Implementation of Information Bottleneck Method for LDPC Decoders

---
Overview: BRAM based Lookup Tables
CNU-IB ROM
CNU-IB Map
1st 9-entry page
2nd 9-entry page
Entry
Indexing
Func.
Page Data
Address
Map
256-entry
5th connected
variable node
E_5
Address
Data
"Check Node" newline (d_{c}=6)
114th 9-entry page
36-bit
(4-bit for each entry)
256-entry
256-entry
256-entry
M_0 M_1 M_2 M_3 M_4 E_5
color red {f^(i)_0( y_0, y_1 )} color red {f^(i)_1( y_0, y_1 )} color red {f^(i)_02( y_0, y_1 )} color red {f^(i)_{d_{c}-3}( y_0, y_1 )}
32x4-bit
32x4-bit
32x4-bit
32x4-bit
CNU-IB RAM

---
CNU-IB ROM Accesses
Specification of BRAM
Page size: 36-bit
Depth: 114
Dual read ports
Read latency: 1 clock cycle
(3,6)-regular code configuration
Quantised message of 4-bit
(dc-2) number of decomposed LUTs
24x24=256 entries, i.e., 1024-bit
Memory utilisation: 15 pages
Total memory utilisation: 114 pages
36
36
Port A
Port B
Port A
CNU-IB ROM
Addr_A
Addr_B
7
7
CNU-IB Map
32
32
32
32
ram_portA[0:7]
ram_portB[0:7]
ram_portC[0:7]
ram_portD[0:7]
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
Qx8=32
ram_portA[0:7]
bank0_portA
bank1_portA
bank2_portA
bank3_portA
bank4_portA
bank5_portA
bank6_portA
bank7_portA

---
Structure of Information Bottleneck LUTs
32x2 Quad Port Distributed RAM (RAM32M) [1]
[1] Guide, User. "Series FPGAs configurable logic block." Xilinx, San Jose, CA 1.7 (7).
[1] Lewandowsky, Jan, and Gerhard Bauch. "Information-optimum LDPC decoders based on the information bottleneck method."Â IEEE AccessÂ 6 (2018): 4054-4071.

---
Structure of Information Bottleneck LUTs
Specification of distributed RAM (Xilinx FPGAs)
Quad-Port 32 x 2-bit RAM (four number of 6-LUTs)
Four duplicated 32x2b RAMs, i.e., port A, B, C and D
One port for synchronous write and asynchronous reads
Three ports for asynchronous reads
Structure of CNU-IB RAM
Concatenation of two RAM32Ms: 4-bit of data bus width
To match size of one quantised message
Construction of one mutual information maximising LUT
22Q entries for each decomposed 2-input LUT, i.e., 256 entries
dc-2 number of decomposed 2-input LUTs
Eight RAM banks to partition 256 entries
Figure 1. Illustration of IB LUTs decomposition [1]
4
tC0 of portA
3
ram_bank_address
[1] Lewandowsky, Jan, and Gerhard Bauch. "Information-optimum LDPC decoders based on the information bottleneck method."Â IEEE AccessÂ 6 (2018): 4054-4071.
2-bit
2-bit
32
depth
32
depth
2
2
4
Bank 7
2-bit
2-bit
32
depth
32
depth
2
2
4
Bank 6
2-bit
2-bit
32
depth
32
depth
2
2
4
Bank 5
2-bit
2-bit
32
depth
32
depth
2
2
4
Bank 4
2-bit
2-bit
32
depth
32
depth
2
2
4
Bank 3
2-bit
2-bit
32
depth
32
depth
2
2
4
Bank 2
2-bit
2-bit
32
depth
32
depth
2
2
4
Bank 1
2-bit
2-bit
32
depth
32
depth
2
2
4
Bank 0
MUX
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
bank0_portA
bank1_portA
bank2_portA
bank3_portA
bank4_portA
bank5_portA
bank6_portA
bank7_portA

---
CNU-IB Map: Bank Interleaving
36
36
Port A
Port B
Port A
CNU-IB ROM
Addr_A
Addr_B
7
7
CNU-IB Map
32
32
32
32
ram_portA[0:7]
ram_portB[0:7]
ram_portC[0:7]
ram_portD[0:7]
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
Q=4
Qx8=32
ram_portA[0:7]
bank0_portA
bank1_portA
bank2_portA
bank3_portA
bank4_portA
bank5_portA
bank6_portA
bank7_portA

---
Entry Indexing Function: IB LUT Access Address
Entry address transalation for one decomposed 2-input LUT
Concatenate two input signals as address
Address bus of RAM32_4bit x 8 banks
RAM bank address: 3-bit
RAM page address: 5-bit
All banks share the same page address
f^i_m( y_0,y_1 ) y_0 y_1 y_0,`y_1,`t_m`in`\{ 0,`1,`...,`2^{Q}-1 \} t_m
alignl "ram_bank_addr"`=`y_1`%`8 newline alignl "ram_page_addr"`=`{ 2 cdot y_0 }+{ y_1 over 8 } newline alignl t_m`=`"RAM32_4b_8"[ "ram_bank_addr" ][ "ram_page_addr" ]
Entry 0
Entry 1
Entry 2
Entry 7
Entry 8
Entry 9
Entry 10
Entry 15
Entry 248
Entry 249
Entry 250
Entry 255
Bank0
Bank1
Bank2
Bank7
4-bit
32
depth
y0
y1
4-bit
4-bit
Page address
Bank address
5-bit
3-bit
Address Mapping:
Address

---
System Architecture
CNU-IB ROM
CNU-IB Map
1st 9-entry page
2nd 9-entry page
Entry
Indexing
Func.
Page Data
Address
Map
256-entry
5th connected
variable node
E_5
Address
Data
"Check Node" newline (d_{c}=6)
114th 9-entry page
36-bit
(4-bit for each entry)
256-entry
256-entry
256-entry
M_0 M_1 M_2 M_3 M_4 E_5
color red {f^(i)_0( y_0, y_1 )} color red {f^(i)_1( y_0, y_1 )} color red {f^(i)_02( y_0, y_1 )} color red {f^(i)_{d_{c}-3}( y_0, y_1 )}
32x4-bit
32x4-bit
32x4-bit
32x4-bit
CNU-IB RAM

---
Block Diagrams and Interfaces: Write
CNU-IB RAM 0
Page Address Gate
addr0
interBank_data
write_addr
addr1
addr0
selector
ram_sel
addr2
‘1’
write_en
ram_clk
addr3
addr1
CNU-IB RAM 1
CNU-IB ROM
CNU-IB Map
interBank_data
36
write_addr
ram_portA
Port A
In_0
ram_portB
‘1’
write_en
Port B
In_1
ram_portC
CNU-IB RAM 2
36
ram_portD
Addr_0
Addr_1
interBank_data
7
write_addr
2
m
addr2
rom_clk
‘1’
write_en
7
CNU-IB RAM 3
Counter
m-bit
ram_sel
interBank_data
addr3
write_addr
m_clk
m`=`lceil log_2( d_c-2 ) rceil
rom_clk
‘1’
write_en
ram_clk
...
0
1
2
3
4
5
14
13
0
Clock Source	Clock Rate
ram_clk	300 MHz
rom_clk	100 MHz
m_clk	20 MHz
ram_clk
0
1
2
3
rom_clk
0
1
m_clk
32
MUX
32
32
32
DEMUX
32
32
32
32
32
Counter
2-bit
Decomposition Clock Generator
5
5
5
5
m

---
Block Diagrams and Interfaces: Read
Entry
Indexing Function
page_addr
y0
M_0
bank_addr
y1
Entry
Indexing Function
CNU-IB RAM 0
page_addr
page_addr
y0
t
Entry
Indexing Function
bank_addr
y1
bank_addr
write_en
‘0’
CNU-IB RAM 1
ram_clk
page_addr
y0
bank_addr
t
y1
page_addr
bank_addr
write_en
‘0’
M_2
M_3
Entry
Indexing Function
CNU-IB RAM 2
CNU-IB RAM 3
page_addr
t
y0
page_addr
page_addr
t
E_5
bank_addr
y1
bank_addr
bank_addr
write_en
‘0’
write_en
‘0’
ram_clk
ram_clk
M_4
4
M_1
4
4
5
3
4
4
5
3
4
4
5
3
5
3
4
4
ram_clk

---
CNU6IB Control Unit
a) Output:
(1) ram_write_en
(2) iter_update
(3) c6ib_rom_rst
b) Input:
(1) sys_clk
(2) rstn
(3) iter_rqst
(4) iter_terminate
Finite State
State 0. IDLE
input: {sys_clk, rstn, iter_rqst, iter_terminate} == {x, 0, 0, 0}
output: {ram_write_en, iter_update, c6ib_rom_rst} == {0, 0, 1}
next step:
{negedge, 1, 1, 1} -> State 1
others -> suspension
State 1. PRELOAD ADDR
input (from State 0): {sys_clk, rstn, iter_rqst, iter_terminate} == {negedge, 1, 1, 0}
output: {ram_write_en, iter_update, c6ib_rom_rst} = {0, 1, 0}
operation:
To give ROM dual-port's corresponding read addresses, i.e., 0x00 and 0x01, at half clock cycle ahead of
ROM-Data-Fetch timing (rising edge of rom_clk).
next step:
{posedge, 1, 1, 0} -> State 2
others -> suspension
State 2. PRELOAD DATA
input (from State 1): {sys_clk, rstn, iter_rqst, iter_terminate} == {posedge, 1, 1, 0}
output: {write_en, iter_update, c6ib_rom_rst} = {0, 1, 0}
operation:
To fetch first two pages' data from ROM, i.e., first 18 entries for RAM.
Then the data will be latched on dual read ports, each of which contributes 36-bit or 9 entries of data.
next step:
{negedge, 1, 1, 0} -> State 3
others -> suspension
State 3. RAM LOAD
input (from State 2): {sys_clk, rstn, iter_rqst, iter_terminate} == {negedge, 1, 1, 0}
output: {write_en, iter_update, c6ib_rom_rst} = {1, 1, 0}
operation:
The CNU-IB Map will partition and latch the first given 72-bit or 18 entries of data in a bank-interleaving
manner, at its three read ports of 32-bit width for each.
next step:
{negedge, 1, 1, 0} -> State 4
others -> suspension
State 4. BATCH WRITE
input (from State 3): {sys_clk, rstn, iter_rqst, iter_terminate} == {negedge, 1, 1, 0}
output {write_en, iter_update, c6ib_rom_rst} = {1, 1, 0}
operation:
Iteratively writing the data into CNU-IB RAMs
next step:
sys_clk in posedge && (iter_rqst == 0 || iter_terminate == 1) -> State 5
{sys_clk, rstn, iter_rqst, iter_terminate} == {negedge, 1, 1, 0} -> State 4
others -> suspension
State 5. FINISH
input (from State 4): {sys_clk, rstn, iter_rqst || iter_terminate} == {posedge, 0, 1}
output: {write_en, iter_update, c6ib_rom_rst} = {0, 0, 1}
operation:
Completing the update of next iteration's data set, then coming back to IDLE status again.
next step:
x -> State 0
CNU-IB Control Unit
Finite State Machine
Input
sys_clk
Rstn
iter_rqst
iter_termination
Output
ram_write_en
iter_update
c6ib_rom_rst
State 0: IDLE
Output: {0, 0, 1}
State 1: PRELOAD_ADDR
Output: {0, 1, 0}
State 2: PRELOAD_DATA
Output: {1, 1, 0}
State 3: RAM_LOAD
Output: {1, 1, 0}
State 4: BATCH_WRITE
Output: {1, 1, 0}
State 5: FINISH
Output: {0, 0, 1}
[Speaker Notes: CNU6IB Control Unit a) Output: (1) ram_write_en (2) iter_update (3) c6ib_rom_rst b) Input: (1) sys_clk (2) rstn (3) iter_rqst (4) iter_terminate Finite State State 0. IDLE input: {sys_clk, rstn, iter_rqst, iter_terminate} == {x, 0, 0, 0} output: {ram_write_en, iter_update, c6ib_rom_rst} == {0, 0, 1} next step: {negedge, 1, 1, 1} -> State 1 others -> suspension State 1. PRELOAD ADDR input (from State 0): {sys_clk, rstn, iter_rqst, iter_terminate} == {negedge, 1, 1, 0} output: {ram_write_en, iter_update, c6ib_rom_rst} = {0, 1, 0} operation: To give ROM dual-port's corresponding read addresses, i.e., 0x00 and 0x01, at half clock cycle ahead of ROM-Data-Fetch timing (rising edge of rom_clk). next step: {posedge, 1, 1, 0} -> State 2 others -> suspension State 2. PRELOAD DATA input (from State 1): {sys_clk, rstn, iter_rqst, iter_terminate} == {posedge, 1, 1, 0} output: {write_en, iter_update, c6ib_rom_rst} = {0, 1, 0} operation: To fetch first two pages' data from ROM, i.e., first 18 entries for RAM. Then the data will be latched on dual read ports, each of which contributes 36-bit or 9 entries of data. next step: {negedge, 1, 1, 0} -> State 3 others -> suspension State 3. RAM LOAD input (from State 2): {sys_clk, rstn, iter_rqst, iter_terminate} == {negedge, 1, 1, 0} output: {write_en, iter_update, c6ib_rom_rst} = {1, 1, 0} operation: The CNU-IB Map will partition and latch the first given 72-bit or 18 entries of data in a bank-interleaving manner, at its three read ports of 32-bit width for each. next step: {negedge, 1, 1, 0} -> State 4 others -> suspension State 4. BATCH WRITE input (from State 3): {sys_clk, rstn, iter_rqst, iter_terminate} == {negedge, 1, 1, 0} output {write_en, iter_update, c6ib_rom_rst} = {1, 1, 0} operation: Iteratively writing the data into CNU-IB RAMs next step: sys_clk in posedge && (iter_rqst == 0 || iter_terminate == 1) -> State 5 {sys_clk, rstn, iter_rqst, iter_terminate} == {negedge, 1, 1, 0} -> State 4 others -> suspension State 5. FINISH input (from State 4): {sys_clk, rstn, iter_rqst || iter_terminate} == {posedge, 0, 1} output: {write_en, iter_update, c6ib_rom_rst} = {0, 0, 1} operation: Completing the update of next iteration's data set, then coming back to IDLE status again. next step: x -> State 0]

---
Evaluation Metrics
"Decoding Throughput"={ Freq times BlockLength } over { "Cycles per Iter" times "Num of Iter"}